## Slide 1: Digital Logic Design
Semester II
FY
Course Code
316U06C203
Jan – May 2026

## Slide 2: Quine McCluskey Minimization Techniques

## Slide 3: Minimization using Quine McClusky Method
List all Minterms
Group Minterms by Number of 1s ( there will be n+1 groups)
Combine Minterms from adjacent groups by eliminating the variable in which they are differing
Repeat Grouping and Combining till no further combinations are possible
The uncombined terms are called Prime Implicants (PIs).
Create a Prime Implicant table with:
  Rows = Prime Implicants
  Columns = Original minterms
  Mark with X where an implicant covers a minterm.
  A Prime Implicant that covers a minterm no other PI covers is called Essential Prime Implicant (EPI). Include all EPIs
  Cover Remaining Minterms if any.

## Slide 4: Minimization using Quine McClusky Method
F(A,B,C,D) = ∑m(0,1,4,5,10,11,13,14,15)
Group Minterms by Number of 1s
Group No | Minterm | Expression | Combine 1 |  | Combine 2 | 
 |  |  | Minterm | expression | Minterm | expression
0 | 0 | 0000 | 0,1 | 000X | 0,1,4,5 | 0X0X
1 | 1 | 0001 | 0,4 | 0X00 | 0,4,1,5 | 0X0X
 | 4 | 0100 |  |  |  | 
2 | 5 | 0101 | 1,5 | 0X01 |  | 
 | 10 | 1010 | 4,5 | 010X |  | 
3 | 11 | 1011 | 5,13 | X101 |  | 
 | 13 | 1101 | 10,11 | 101X |  | 
 | 14 | 1110 | 10,14 | 1X10 | 10,11,14,15 | 1X1X
4 | 15 | 1111 | 11,15 | 1X11 | 10,14,11,15 | 1X1X
 |  |  | 13,15 | 11X1 |  | 
 |  |  | 14,15 | 111X |  | 

## Slide 5: Minimization using Quine McClusky Method
F(A,B,C,D) = ∑m(0,1,4,5,10,11,13,14,15)
Prime Implicants P1 = 5,13 = X101 , P2= 13,15 = 11X1,
P3 = 0,1,4,5 =0X0X P4 = 10,11,14,15= 1X1X
Therefore P3 and P4 are essential prime Implicants
PI/ Minterms | 0 | 1 | 4 | 5 | 10 | 11 | 13 | 14 | 15
P1 = 5,13 |  |  |  | * |  |  | * |  | 
P2 = 13,15 |  |  |  |  |  |  | * |  | *
P3 = 0,1,4,5 | * | * | * | * |  |  |  |  | 
P4 = 10,11,14,15 |  |  |  |  | * | * |  | * | *
 | P3 | P3 | P3 | P1,P3 | P4 | P4 | P1,P2 | P4 | P2,P4

## Slide 6: Minimization using Quine McClusky Method
With choice of P3 and P4 Minterms covered are 0,1,4,5,10,11,14,15
Minterm 13 is covered either by P1 or by P2
F = P1+P3+P4 or F = P2+P3+P4
F = BC’D+A’C’+AC
OR
F = ABD+A’C’+AC
AB/CD | 00 | 01 | 11 | 10
00 | 1 | 1 | 0 | 0
01 | 1 | 1 | 1 | 0
11 | 0 | 0 | 1 | 1
10 | 0 | 0 | 1 | 1

## Slide 7: Minimization using Quine McClusky Method
F(A,B,C,D) = Σ m (0, 1, 3, 8, 9, 13, 14, 15, 16, 17, 19, 24, 25, 27, 31)
Group No | Minterm | Expression | Gr | Combine 1 |  | Gr | Combine 1 | 
0 | 0 | 00000 | 0,1 | 0,1 | 0000X | 2,3 | 3,19 | X0011
1 | 1 | 00001 |  | 0,8 | 0X000 |  | 9,13 | 01X01
 | 8 | 01000 |  | 0,16 | X0000 |  | 9,25 | X1001
 | 16 | 10000 | 1,2 | 1,3 | 000X1 |  | 17,19 | 100X1
2 | 3 | 00011 |  | 1,9 | 0X001 |  | 17,25 | 1X001
 | 9 | 01001 |  | 1,17 | X0001 |  | 24,25 | 1100X
 | 17 | 10001 |  | 8,9 | 0100X | 3,4 | 13,15 | 011X1
 | 24 | 11000 |  | 8,24 | X1000 |  | 14,15 | 0111X
3 | 13 | 01101 |  | 16,17 | 1000X |  | 19,27 | 1X011
 | 14 | 01110 |  | 16,24 | 1X000 |  | 25,27 | 110X1
 | 19 | 10011 |  |  |  | 4,5 | 15,31 | X1111
 | 25 | 11001 |  |  |  |  | 27,31 | 11X11
4 | 15 | 01111 |  |  |  |  |  | 
 | 27 | 11011 |  |  |  |  |  | 
5 | 31 | 11111 |  |  |  |  |  | 

## Slide 8: Minimization using Quine McClusky Method
Gr | Combine 1 |  | Gr | Combine 1 |  | Gr | Combine 2 |  | Gr | Combine 2 | 
0&1 | 0,1 | 0000X | 2&3 | 3,19 | X0011 | 0-1-2 | 0,1,8,9 | 0X00X | 2-3-4 | 17,19,25,27 | 1X0X1
 | 0,8 | 0X000 |  | 9,13 | 01X01 |  | 0,8,1,9 |  |  | 17,25,19,27 | 
 | 0,16 | X0000 |  | 9,25 | X1001 |  | 0,1,16,17 | X000X | 3-4-5 | - | 
1&2 | 1,3 | 000X1 |  | 17,19 | 100X1 |  | 0,16,1,17 |  |  |  | 
 | 1,9 | 0X001 |  | 17,25 | 1X001 |  | 0,16,8,24 | XX000 |  |  | 
 | 1,17 | X0001 |  | 24,25 | 1100X |  | 0,8,16,24 |  |  |  | 
 | 8,9 | 0100X | 3&4 | 13,15 | 011X1 | 1-2-3 | 1,3,17,19 | X00X1 |  |  | 
 | 8,24 | X1000 |  | 14,15 | 0111X |  | 1,17,3,19 |  |  |  | 
 | 16,17 | 1000X |  | 19,27 | 1X011 |  | 1,9,17,25 | XX001 |  |  | 
 | 16,24 | 1X000 |  | 25,27 | 110X1 |  | 1,17,9,25 |  |  |  | 
 |  |  | 4&5 | 15,31 | X1111 |  | 8,9,24,25 | X100X |  |  | 
 |  |  |  | 27,31 | 11X11 |  | 8,24,9,25 |  |  |  | 
 |  |  |  |  |  |  | 16,17,24,25 | 1X00X |  |  | 
 |  |  |  |  |  |  | 16,24,17,25 |  |  |  | 

## Slide 9: Minimization using Quine McClusky Method
PI from Combine 1 |  | Gr | Combine 2 |  | Gr | Combine 2 |  | Gr | Combine 3 | 
9,13 | 01X01 | 0-1-2 | 0,1,8,9 | 0X00X | 2-3-4 | 17,19,25,27 | 1X0X1 | 0-1-2-3 | 0,1,8,9, 16,17,24,25 | XX00X
13,15 | 011X1 |  | 0,8,1,9 |  |  | 17,25,19,27 |  |  | 0,1,16,17,8,9,24,25 | 
14,15 | 0111X |  | 0,1,16,17 | X000X | 3-4-5 | - |  |  | 0,16,8,24,1,17,9,25 | 
15,31 | X1111 |  | 0,16,1,17 |  |  |  |  | 1-2-3-4 | - | 
27,31 | 11X11 |  | 0,16,8,24 | XX000 |  |  |  |  |  | 
 |  |  | 0,8,16,24 |  |  |  |  |  |  | 
 |  | 1-2-3 | 1,3,17,19 | X00X1 |  |  |  |  |  | 
 |  |  | 1,17,3,19 |  |  |  |  |  |  | 
 |  |  | 1,9,17,25 | XX001 |  |  |  |  |  | 
 |  |  | 1,17,9,25 |  |  |  |  |  |  | 
 |  |  | 8,9,24,25 | X100X |  |  |  |  |  | 
 |  |  | 8,24,9,25 |  |  |  |  |  |  | 
 |  |  | 16,17,24,25 | 1X00X |  |  |  |  |  | 
 |  |  | 16,24,17,25 |  |  |  |  |  |  | 

## Slide 10: Minimization using Quine McClusky Method
F(A,B,C,D) = Σ m (0, 1, 3, 8, 9, 13, 14, 15, 16, 17, 19, 24, 25, 27, 31)
Prime Implicants P1 = 9,13 = 01X01 P2 = 13,15 = 011X1 P3 =14,15 = 0111X
P4 = 15,31=X1111 P5 = 27,31 =11X11 P6 = 1,3,17,19 = X00X1
P7 = 17,19,25,27 = 1X0X1 P8 = 0,1,8,9, 16,17,24,25 = XX00X
PI/ Minterms | 0 | 1 | 3 | 8 | 9 | 13 | 14 | 15 | 16 | 17 | 19 | 24 | 25 | 27 | 31
P1 = 9,13 |  |  |  |  | * | * |  |  |  |  |  |  |  |  | 
P2 = 13,15 |  |  |  |  |  | * |  | * |  |  |  |  |  |  | 
P3 = 14,15 |  |  |  |  |  |  | * | * |  |  |  |  |  |  | 
P4 = 15,31 |  |  |  |  |  |  |  | * |  |  |  |  |  |  | *
P5 = 27,31 |  |  |  |  |  |  |  |  |  |  |  |  |  | * | *
P6 = 1,3,17,19 |  | * | * |  |  |  |  |  |  | * | * |  |  |  | 
P7 = 17,19,25,27 |  |  |  |  |  |  |  |  |  | * | * |  | * | * | 
P8 = 0,1,8,9,16,17,24,25 | * | * |  | * | * |  |  |  | * | * |  | * | * |  | 
EPI | P8 |  | P6 | P8 |  |  | P3 |  | P8 |  |  | P8 |  |  | 

## Slide 11: Minimization using Quine McClusky Method
F(A,B,C,D) = Σ m (0, 1, 3, 8, 9, 13, 14, 15, 16, 17, 19, 24, 25, 27, 31)
F = P3+P6+P8 consider P5 for 27 and 31 , P1/P2 for 13
F = P1+P3+P5+P6+P8 or P2+P3+P5+P6+P8
PI/ Minterms | 0 | 1 | 3 | 8 | 9 | 13 | 14 | 15 | 16 | 17 | 19 | 24 | 25 | 27 | 31
P1 = 9,13 |  |  |  |  | * | * |  |  |  |  |  |  |  |  | 
P2 = 13,15 |  |  |  |  |  | * |  | * |  |  |  |  |  |  | 
P3 = 14,15 |  |  |  |  |  |  | * | * |  |  |  |  |  |  | 
P4 = 15,31 |  |  |  |  |  |  |  | * |  |  |  |  |  |  | *
P5 = 27,31 |  |  |  |  |  |  |  |  |  |  |  |  |  | * | *
P6 = 1,3,17,19 |  | * | * |  |  |  |  |  |  | * | * |  |  |  | 
P7 = 17,19,25,27 |  |  |  |  |  |  |  |  |  | * | * |  | * | * | 
P8 = 0,1,8,9,16,17,24,25 | * | * |  | * | * |  |  |  | * | * |  | * | * |  | 
EPI | P8 |  | P6 | P8 |  |  | P3 |  | P8 |  |  | P8 |  |  | 
Covered Minterms | * | * | * | * | * |  | * | * | * | * | * | * | * |  | 
Remaining Minterms |  |  |  |  |  | * |  |  |  |  |  |  |  | * | *

## Slide 12: Minimization using Quine McClusky Method
F(A,B,C,D) = Σ m (0,2,5,7,8, 9,10,11, 13,15)
Group No | Minterm | Expression | Gr | Combine 1 |  | Gr | Combine 1 | 
0 | 0 | 0000 | 0,1 | 0,2 | 00X0 | 3,4 | 7,15 | X111
1 | 2 | 0010 |  | 0,8 | X000 |  | 11,15 | 1X11
 | 8 | 1000 | 1,2 | 2,10 | X010 |  | 13,15 | 11X1
2 | 5 | 0101 |  | 8,9 | 100X |  |  | 
 | 9 | 1001 |  | 8,10 | 10X0 |  |  | 
 | 10 | 1010 | 2,3 | 5,7 | 01X1 |  |  | 
3 | 7 | 0111 |  | 5,13 | X101 |  |  | 
 | 11 | 1011 |  | 9,11 | 10X1 |  |  | 
 | 13 | 1101 |  | 9,13 | 1X01 |  |  | 
4 | 15 | 01111 |  | 10,11 | 101X |  |  | 

## Slide 13: Minimization using Quine McClusky Method
F(A,B,C,D) = Σ m (0,2,5,7,8, 9,10,11, 13,15)
Gr | Combine 1 |  | Gr | Combine 1 |  | Gr | Combine 2 |  | 
0,1 | 0,2 | 00X0 | 3,4 | 7,15 | X111 | 0-1-2 | 0,2,8,10 | X0X0 | P1
 | 0,8 | X000 |  | 11,15 | 1X11 |  | 0,8,2,10 |  | 
1,2 | 2,10 | X010 |  | 13,15 | 11X1 | 1-2-3 | 8,9,10,11 | 10XX | P2
 | 8,9 | 100X |  |  |  |  | 8,10,9,11 |  | 
 | 8,10 | 10X0 |  |  |  | 2-3-4 | 5,7,13,15 | X1X1 | P3
2,3 | 5,7 | 01X1 |  |  |  |  | 5,13,7,15 |  | 
 | 5,13 | X101 |  |  |  |  | 9,13,11,15 | 1XX1 | P4
 | 9,11 | 10X1 |  |  |  |  | 9,11,13,15 |  | 
 | 9,13 | 1X01 |  |  |  |  |  |  | 
 | 10,11 | 101X |  |  |  |  |  |  | 

## Slide 14: Minimization using Quine McClusky Method
F(A,B,C,D) = Σ m (0,2,5,7,8, 9,10,11, 13,15)
Prime Implicants P1 = 0,2,8,10 = X0X0 P2 =8,9,10,11 = 10XX
P3 =5,7,13,15 = X1X1 P4 = 9,13,11,15 = 1XX1
Reamining minterms ( 9 and 11) can be covered either by P2 or P4
F = P1+P3+P2 = P1+P3+P4
= B’D’+BD+AB’ = B’D’+BD+AD
PI/ Minterms | 0 | 2 | 5 | 7 | 8 | 9 | 10 | 11 | 13 | 15
P1 = 0,2,8,10 | * | * |  |  | * |  | * |  |  | 
P2 =8,9,10,11 |  |  |  |  | * | * | * | * |  | 
P3 =5,7,13,15 |  |  | * | * |  |  |  |  | * | *
P4 = 9,13,11,15 |  |  |  |  |  | * |  | * | * | *
EPI | P1 | P1 | P3 | P3 |  |  |  |  |  | 
Covered Minterms by EPI | * | * | * | * | * |  | * |  | * | *
Remaining Minterms |  |  |  |  |  | * |  | * |  | 

## Slide 15: Minimization using Quine McClusky Method
F(A,B,C,D) = Σ m (0, 1, 3, 8, 9, 13, 14, 15, 16, 17, 19, 24, 25, 27, 31)
F = P3+P6+P8 consider P5 for 27 and 31 , P1/P2 for 13
F = P1+P3+P5+P6+P8 or P2+P3+P5+P6+P8
PI/ Minterms | 0 | 1 | 3 | 8 | 9 | 13 | 14 | 15 | 16 | 17 | 19 | 24 | 25 | 27 | 31
P1 = 9,13 |  |  |  |  | * | * |  |  |  |  |  |  |  |  | 
P2 = 13,15 |  |  |  |  |  | * |  | * |  |  |  |  |  |  | 
P3 = 14,15 |  |  |  |  |  |  | * | * |  |  |  |  |  |  | 
P4 = 15,31 |  |  |  |  |  |  |  | * |  |  |  |  |  |  | *
P5 = 27,31 |  |  |  |  |  |  |  |  |  |  |  |  |  | * | *
P6 = 1,3,17,19 |  | * | * |  |  |  |  |  |  | * | * |  |  |  | 
P7 = 17,19,25,27 |  |  |  |  |  |  |  |  |  | * | * |  | * | * | 
P8 = 0,1,8,9,16,17,24,25 | * | * |  | * | * |  |  |  | * | * |  | * | * |  | 
EPI | P8 |  | P6 | P8 |  |  | P3 |  | P8 |  |  | P8 |  |  | 
Covered Minterms | * | * | * | * | * |  | * | * | * | * | * | * | * |  | 
Remaining Minterms |  |  |  |  |  | * |  |  |  |  |  |  |  | * | *